## Slide 1: IoT on premises
How to start an adventure with
&
Mariusz Krzanowski

## Slide 2: Goals of the presentation
Primary goals
How to begin an adventure with IoT?
What is the minimum set of devices needed to start the fun?
Where are the limitations of current IoT devices?
Secondary Goals
Extend our current architectural knowledge, by reviewing new solutions.
Familiarizing with other approaches of solving problems.

## Slide 3: About ME
Employed in IT since 1999
  Developer / Architect / Team Leader
  Now: Senior Software Developer @ Demant Technology Centre
Experienced in many technologies
  .NET, SQL, SharePoint, BizTalk, Google Cloud, Android, SCCM Active Directory, Web Development … 20 years is long time 
I like to share my knowledge with others – you can meet me at Warszawska Grupa .NET (WG-NET)

## Slide 4: Agenda:
What devices will be presented today?
What is Node-Red?
  Workflow engine
  What do we have out of the box
  Key components
What is Mosquitto?
  MQTT
  Message Broker
  Key components
How to start an adventure with Workflow Engine and MQTT
A lot of practical examples!


## Slide 5: Featured devices
WI-FI Router (out of scope)
Raspberry PI Zero W (€12-€17)
ESP8266-12E board (~€6)
ESP8266-01 (~€3)
SONOFF S20 (~17€)
Diodes, thermometers, transistors, resistors, toggle switches … (~€0.1 each)
Various power supplies
Bonus 

## Slide 6: What is Node-Red?
Developed originally by IBM as a flow design tool.
Web browser based application. Server side written in NodeJS.
Dashboard delivers: buttons, gauges and charts.
It is open-source since September 2013.
Multiple out of the box nodes - including MQTT.
JavaScript based functions.
NOTE: Preinstalled on Raspberry PI – update suggested.
https://nodered.org/

## Slide 7: FYI: How to INSTALL Node-Red
sudo apt-get upate
sudo apt-get upgrade
sudo apt-get install nodered
sudo systemctl enable nodered.service
NOTE: from UI install: node-red-dashboard

## Slide 8: DEMO (1) Node-Red
3 types of nodes
  Input
  Output
  Transform
Inject Node
Debug Node

## Slide 9: DEMO (1) Node-Red – first flow

## Slide 10: DEMO (1) Node-Red – First flow
http://192.169.168.10:1880/
DEMO TIME 

## Slide 11: DEMO (2) Raspberry PI and DIODE

## Slide 12: DEMO (2) - Raspberry PI W – pinout
https://raspberrypi.stackexchange.com/questions/83610/gpio-pinout-orientation-raspberypi-zero-w

## Slide 13: DEMO (2) Circuit schema
GPIO21
GND
Longer leg is a positive electrode (+)
3.3 KΩ

## Slide 14: DEMO (2) Raspberry PI and DIODE

## Slide 15: DEMO (2) Raspberry PI and DIODE

## Slide 16: DEMO (2) - breadboard Photo
DEMO TIME 

## Slide 17: What is Mosquitto™
Message broker that implements MQTT protocol.
MQTT stands for Message Queuing Telemetry Transport.
NOTE: Available on Raspberry PI.
Created by Roger Light in 2009.
https://mosquitto.org/
NOTE! MQTT protocol is used e.g. by:
Facebook Messenger
Microsoft Azure IoT Hub
Amazon Web Services

## Slide 18: MQTT Broker architecture
Publisher 1
Publisher 2
Publisher N
.
.
.
.
.
.
Subscriber 1
Subscriber 2
Subscriber N
.
.
.
.
.
.
Communication process is asynchronous.
Publisher does not ‘know’ any subscribers.

## Slide 19: MQTT – Domain language
Payload – array of bytes by default. Strings or JSON is used for better readability.
Topic – Like URI determines a category to which a message belongs. NOTE! Topics are case sensitive!
Topic examples:
  /lamp/kitchen/status
  /lamp/kitchen/command
  /heater/dining-room/temperature
Publisher can publish messages for predefined topic.
Subscriber can subscribe for messages under specified topics.
Wildcards help to subscribe to multiple topics:
  # can be used as a wildcard for all remaining levels of hierarchy e.g. /lamp/#
  + can be used as a wildcard for a single level of hierarchy e.g. /+/kitchen/+

## Slide 20: FYI: How to INSTAL Mosquitto?
sudo apt-get upate
sudo apt-get upgrade
sudo apt-get install mosquitto
sudo apt-get install mosquitto-clients
sudo mosquitto_passwd -c /etc/mosquitto/passwd IotUserMqtt
sudo systemctl enable mosquitto

## Slide 21: Demo(3) – MQTT on node red only
DEMO TIME

## Slide 22: Demo (4) – MQTT ON ESP8266-E12
MQTT Client
MQTT Broker
WI-FI Router

## Slide 23: Demo (4) – MQTT ON ESP8266-E12
3.3 V
GND
10KΩ
3.3 KΩ
D1
D3

## Slide 24: Demo (4) – MQTT ON ESP8266-E12

## Slide 25: Demo (4) – MQTT ON ESP8266-E12
Source code:
src\Arduino\DiodeAndButton

## Slide 26: Demo (4) – MQTT ON ESP8266-E12

## Slide 27: Demo (4) – MQTT ON ESP8266-E12
DEMO TIME

## Slide 28: Quiz
Question:
  How many wires does 1-Wire Protocol use? NOTE. It is a tricky question.

## Slide 29: Quiz
Question:
  How many wires does 1-Wire Protocol use? NOTE. It is a tricky question.
Answer:
3 wires in normal mode: VCC, DATA, GND
2 wires in parasite mode: VCC – DATA, GND

## Slide 30: 1-Wire protocol (Parasite mode)
DATA
Master node
GND
VCC
S1
Slave node
S2
Slave node
SN
Slave node
This ‘single’ wire allows you to connect multiple devices to a single controller.

## Slide 31: Demo (5) – Thermometer
3 V
GND
10KΩ
3.3 KΩ
D1
D3
D7
2 x 1KΩ
DS18B20

## Slide 32: Demo (5) – Thermometer
3 V
GND
10KΩ
3.3 KΩ
D1
D3
D7
2 x 1KΩ
DS18B20

## Slide 33: Demo(5) Thermometer

## Slide 34: Demo(5) Thermometer
GND
Data Line
VCC
Thermometer

## Slide 35: Demo(5) Thermometer
DEMO TIME

## Slide 36: Sonoff S20
SONOFF is a ‘smart’ socket
It uses ESP8266-01S SoC (System on chip).
You can manage it by Android or iOS application.
You can hack it using Arduino and small hooks.

## Slide 37: Demo(6) Sonoff S20
WARNING !!!
HIGH VOLTAGE !!!

## Slide 38: Demo(6) Sonoff S20
WARNING !!!
HIGH VOLTAGE !!!
GND
GPIO 0
TX
RX
3.3V

## Slide 39: Demo(6) Sonoff S20
WARNING !!!
HIGH VOLTAGE !!!
GND
GPIO 0
TX
RX
3.3V
NOTE
You need to connect TX  RX and RX TX on your serial port adapter. ESP chipset supports only 3.3 volts. Your RS-232 adapter must support 3.3 volts on input and output ports.

## Slide 40: Demo(6) Sonoff S20

## Slide 41: Demo(6) Sonoff S20
DEMO TIME 

## Slide 42: BONUS (1) BLE - Intruder

## Slide 43: BONUS (2) MQTT & VOICE CLIENT
Aragorn. Switch on the red light.

## Slide 44: BONUS (3) Smart LAMP
What will happen when you change initial product purpose and extend its usability?

## Slide 45: BONUS (3) Smart LAMP
4,7K Ω
4,7K Ω
B-C-E
I–G-O
GPIO2

## Slide 46: Summary
Node-Red™ and Mosquitto™ are really easy to use.
Both products have been on the market for long and they represent mature solutions.
To start you need to spend less than €30 plus your time.
Visual Studio Code™ and PlatformIO™ make an easy entry level.

## Slide 47: References
Andreas Spiess https://www.youtube.com/channel/UCu7_D0o48KbfhpEohoP7YSQ
GreatScott! https://www.youtube.com/user/greatscottlab
Richard Wenner https://www.youtube.com/user/dicktonybo
bitluni's lab https://www.youtube.com/user/bitlunislab
Kevin Darrah https://www.youtube.com/user/kdarrah1234
Electronoobs https://www.youtube.com/channel/UCjiVhIvGmRZixSzupD0sS9Q
Ben Eater https://www.youtube.com/channel/UCS0N5baNlQWJCUrhCEo8WlA
AUTODESK ® TINKERCAD™ https://www.tinkercad.com/circuits

## Slide 48: Where you can find me?
Web
  https://lastboardingcall.pl
  https://mrmatrix.net
GitHub
  https://github.com/MariuszKrzanowski
Tweeter
  @KrzanowskiM
Meetups
  Warszawska Grupa .NET
Mariusz Krzanowski

## Slide 49
Q & A

## Slide 50
Thank you


## Slide 51: Where you can find me?
Web
  https://lastboardingcall.pl
  https://mrmatrix.net
GitHub
  https://github.com/MariuszKrzanowski
Tweeter
  @KrzanowskiM
Meetups
  Warszawska Grupa .NET
Mariusz Krzanowski